## Slide 1
EQAAB · MISSION CONTROL
CALLSIGN EQB-01
PROJECT ID 503593
2025 / 2026
◇ CAPSTONE II · TAIF UNIVERSITY · 2026 ◇
EQAAB
عقاب
Intelligent Autonomous Aerial Surveillance System
ENGINEERING TEAM
Abdulrahman Al-otaibi · Turki Al-otaibi Saeed Al-harthi · Rayan Al-ghamdi Hossain Al-hubailee · Mohammed Al-sharif Omar Al-anzi
FACULTY SUPERVISOR
Dr. Ahmed bin Mahfoudh College of Computers & IT Taif University, KSA
LAT 21.4373°N
LON 40.5127°E
ALT 1879M
EQAAB / CAPSTONE II / 2026 — V1.0

## Slide 2
EQAAB · AGENDA
SECTION 02 / 24
OPS BRIEFING
02
BRIEFING OUTLINE
Agenda / 24 segments
A complete walkthrough of design, build, test, and field validation of the Eqaab platform.
DURATION
~45 MIN
01 Title & Team
09 Hardware Stack
17 Results & Performance
02 Agenda
10 ROS 2 Software Stack
18 Live Demo
03 Project Recap
11 AI Detection Pipeline
19 Cost Analysis
04 Problem Statement
12 IFF System
20 Objectives vs Achieved
05 Literature & Gap
13 Backend & Comms
21 Challenges & Solutions
06 Objectives & KPIs
14 GCS Dashboard
22 Future Work
07 Real-World Use Cases
15 Training & Dataset
23 Conclusion
08 System Architecture
16 Testing Methodology
24 Q & A
FRAME 02
SECTION_INDEX
EQAAB · BRIEFING

## Slide 3
EQAAB · RECAP
SECTION 03 / 24
03
WHERE WE LEFT OFF → WHERE WE ARE
Project Recap
Capstone I delivered a simulated prototype. Capstone II delivers a deployed, real-hardware system flying real missions.
PHASE SHIFT
SIM → FIELD
◇ CAPSTONE I · 2024 / 2025
Concept & Simulation
◐
Gazebo simulation
Virtual drone, autonomous waypoint flight in SITL
◐
Basic YOLO prototype
Off-the-shelf detection on recorded footage
◐
System design on paper
Block diagrams, sensor selection, requirements
◐
No physical hardware
No flight, no live communication, no real model
● CAPSTONE II · 2025 / 2026
Built. Trained. Flying.
●
Real assembled drone
Carbon-fiber airframe, Pixhawk + RPi5 + Pi Cam
●
Full ROS 2 software stack
Mission FSM, detection, IFF, alert publisher
●
Trained YOLOv8 model
Custom dataset, 94.3% mAP@50, 8.3 FPS edge
●
Deployed cloud backend
FastAPI + PostgreSQL + WSS over 4G LTE
●
Live GCS dashboard
React + Leaflet, real-time alerts & commands
PHASE TRANSITION
EQAAB · RECAP

## Slide 4
EQAAB · THREAT MODEL
SECTION 04 / 24
04
WHY THIS MATTERS
The Problem
Today's wide-area surveillance is built on fixed sensors and tired human operators — both fail exactly when threats become unconventional.
FAILURE MODES
4 IDENTIFIED
01
Fixed-camera blind spots
Static CCTV cannot cover wide, irregular terrain — borders, holy-site perimeters, remote infrastructure. Every fixed installation creates predictable, exploitable gaps in coverage.
02
Operator fatigue
Human watch-standers monitoring dozens of feeds miss critical events as attention degrades over hours. Vigilance decrements are well-documented and unavoidable.
03
Radar can't see small UAVs
Traditional radar is tuned for large aircraft. Small, low-altitude drones present a radar cross-section close to noise — they pass under conventional air defense entirely undetected.
04
Piloted UAVs replicate the fatigue problem
Existing deployed UAV solutions require dedicated human pilots per airframe — recreating the same fatigue and scaling bottleneck the system was meant to eliminate.
THREAT VECTORS · 4
EQAAB · PROBLEM

## Slide 5
EQAAB · LITERATURE
SECTION 05 / 24
05
PRIOR ART & RESEARCH GAP
Literature Review
Each related work covers a slice. None integrate detection, autonomy, GPS-tagged alerts, IFF, and a live operator interface into one cohesive system.
STUDIES REVIEWED
5 + 1
REFERENCE
VEHICLES
HUMANS
DRONES
AUTONOMOUS
GPS
GCS UI
IFF
Yun et al. — Multi-UAV RL
—
—
—
✓
✓
—
—
Guettala et al. — Thermal human detection
—
✓
—
—
—
—
—
Yasmine et al. — Anti-drone YOLOv7
—
—
✓
—
—
—
—
Aydin & Singha — Drone detection YOLOv5
—
—
✓
—
—
—
—
Ghazlane et al. — YOLOv7 + DeepSort
✓
✓
—
—
—
—
—
EQAAB (this work)
✓
✓
✓
✓
✓
✓
✓
Research gap: no published work delivers an end-to-end autonomous surveillance UAV with multi-class onboard detection, IFF classification, and an operator-facing GCS — all on commodity hardware.
GAP IDENTIFIED
EQAAB · LITERATURE

## Slide 6
EQAAB · OBJECTIVES
SECTION 06 / 24
06
WHAT SUCCESS LOOKS LIKE
Objectives & KPIs
Five measurable goals, each tied to a verifiable performance indicator and an evidence source.
KPIS
5 / 5
01
Autonomous mission execution
A complete flight loop — takeoff, waypoint traversal, observation, and return-to-home — executed end-to-end with zero operator input.
FSM · WAYPOINTS · RTH
02
Onboard real-time detection
Sustained inference at ≥ 5 FPS on the edge device with no cloud round-trip. Detection latency must stay bounded even under thermal load over a full mission.
RPI5 · YOLOV8N
03
IFF classification
Every drone-class detection routed through a deterministic Friendly-vs-Unknown decision with fail-safe defaults toward UNKNOWN on any uncertainty.
REGISTRY LOOKUP
04
GPS-tagged alerts over 4G LTE
Detection → alert → GCS render in under 3 seconds , end-to-end, including network hops. Payload is structured JSON over WSS — no video streaming.
WSS · JSON · TLS
05
Live GCS dashboard
A single operator pane with live map, telemetry, alert feed, and commands — updating in real time as the drone flies and detects.
REACT · LEAFLET
KPI MATRIX
EQAAB · OBJECTIVES

## Slide 7
EQAAB · DEPLOYMENT
SECTION 07 / 24
07
WHERE EQAAB EARNS ITS KEEP
Real-World Use Cases
Three deployment scenarios that drove the requirements — and that the platform is built to serve from day one.
MISSION TYPES
3 PRIMARY
Scenario 01
Hajj Season Security
Aerial overwatch of dense pilgrim crowds and unauthorized drone activity around Makkah and the holy sites — coverage no fixed sensor array can match.
Scenario 02
Border Surveillance
Wide-area perimeter patrol across remote terrain where fixed cameras and radar coverage are economically and operationally infeasible.
Scenario 03
Critical Infrastructure
Persistent surveillance over power plants, airports, refineries, and restricted facilities — including detection of small unauthorized UAVs entering protected airspace.
OPS THEATERS
EQAAB · USE CASES

## Slide 8
EQAAB · ARCHITECTURE
SECTION 08 / 24
08
END-TO-END SIGNAL FLOW
System Architecture
Three tiers — drone edge, cloud backend, operator interface — connected over 4G LTE with structured JSON only.
TIERS
3 LAYERS
DRONE EDGE · ONBOARD
CLOUD BACKEND · REGIONAL
GCS · OPERATOR
SENSOR
Pi Camera 12MP
CSI · 1920×1080 @ 30fps
COMPUTE
Raspberry Pi 5
ARM A76 · 8GB · ROS 2
FLIGHT CTRL
Pixhawk · PX4
MAVROS bridge · GPS · IMU
RELAY
FastAPI
WSS endpoint · auth · broadcast
PERSISTENCE
PostgreSQL
Alert history · telemetry log
INTERFACE
React Dashboard
Leaflet map · alert feed · telemetry
OPERATOR
Command Panel
RTH · Takeoff · Land · Waypoints
DATA POLICY
Only structured JSON alerts and telemetry cross the LTE link — no video streaming. Bandwidth requirement drops by approximately 95%.
SIGNAL FLOW · 3-TIER
EQAAB · ARCHITECTURE

## Slide 9
EQAAB · AIRFRAME
SECTION 09 / 24
09
BILL OF MATERIALS & FLIGHT ENVELOPE
Hardware Stack
Off-the-shelf components, integrated and tuned. Production-grade behaviour from commodity hardware.
COMPONENTS
8 SUBSYSTEMS
A · BILL OF MATERIALS
Frame
Carbon-fiber quadcopter · 450mm wheelbase
Flight Controller
Pixhawk · PX4 firmware · 32-bit ARM
Companion Computer
Raspberry Pi 5 · Quad-core A76 · 8GB RAM
Camera
Pi Camera Module · 12MP CSI
GPS
u-blox M8N · ±2m accuracy
Comms
4G LTE USB dongle · global reach
Battery
LiPo 4S 5000mAh
RC Backup
2.4GHz receiver · manual override
B · FLIGHT SPECIFICATIONS
ALTITUDE
~50 m
FLIGHT TIME
15–20 min
RANGE
∞ 4G
GEOFENCE
Polygon
FAILSAFE
RTH @ 30%
📷
PHOTO PLACEHOLDER
Insert hero photograph of the fully assembled Eqaab drone — propellers, gimbal, antenna mast visible.
REF · EQB-HW-01
WEIGHT 1.8KG
THRUST/W 2.4
EQAAB · HARDWARE

## Slide 10
EQAAB · ROS 2 STACK
SECTION 10 / 24
10
SOFTWARE ARCHITECTURE · ONBOARD
ROS 2 Node Graph
Four cooperating nodes orchestrate mission, perception, identification, and uplink.
NODES
4 + MAVROS
01 · CONTROL
mission_manager
FSM · waypoints · commands
/mission/state · /cmd
02 · PERCEPTION
detection_node
YOLOv8 · OpenCV · DeepSORT
/detections
03 · IDENTIFICATION
iff_node
Registry lookup · classification
/iff/classified
04 · UPLINK
alert_publisher
WebSocket · telemetry · JSON
→ wss://eqaab.cloud
MAVROS BRIDGE
MAVLink ↔ ROS 2
Pose · GPS · battery · commands
/mavros/...
FLIGHT HARDWARE
Pixhawk · PX4
ROS 2 HUMBLE
DDS · CYCLONE
EQAAB · SOFTWARE

## Slide 11
EQAAB · PERCEPTION
SECTION 11 / 24
11
FROM PIXELS TO GPS-TAGGED ALERTS
AI Detection Pipeline
A dual-model perception stack with tracking, GPS fusion, and identity classification — all on the edge device.
MODELS
2 · PARALLEL
INPUT
Camera Frame
1920×1080 · 30fps
MODEL A
YOLOv8n.pt
COCO · Person · Car
MODEL B
best.pt
Custom · Drone
FUSE
Merge + Filter
conf ≥ 0.45
TRACK
DeepSORT
Track ID · Kalman
GEO-REF
GPS Fusion
pixel → lat / lon
FRIENDLY
Discard
no alert raised
UNKNOWN
Alert ↑
GPS-tagged · uplinked
DESIGN NOTE
Dual-model architecture adopted to prevent catastrophic forgetting — single-model fine-tuning caused measurable degradation of COCO classes during early experiments.
EDGE INFER · 8.3 FPS
EQAAB · PERCEPTION

## Slide 12
EQAAB · IFF LOGIC
SECTION 12 / 24
12
IDENTIFICATION FRIEND OR FOE
IFF Decision Logic
A deterministic, fail-safe decision tree. Persons and cars never authenticate. Drones do — or get flagged.
FAIL-SAFE
→ UNKNOWN
Detected target
Is it a drone?
CLASS CHECK
PERSON · CAR
→ UNKNOWN
never authenticates
DRONE DETECTED
Query identifier
Signal received?
NO SIGNAL
→ UNKNOWN
comms timeout
Registry match?
REGISTRY HIT
→ FRIENDLY
discard · no alert
NO MATCH
→ UNKNOWN
unrecognized ID
FAIL-SAFE
Every failure path — class mismatch, missing signal, registry miss — defaults to UNKNOWN. The system raises false alerts rather than miss a threat.
DETERMINISTIC LOGIC
EQAAB · IFF

## Slide 13
EQAAB · COMMS LAYER
SECTION 13 / 24
13
CLOUD RELAY & PERSISTENCE
Backend & Communication
A thin, opinionated cloud tier — relay, persist, broadcast. Nothing more.
PROTOCOL
WSS · TLS
ARCHITECTURE
Alert Publisher
4G · WSS · TLS
FastAPI relay
PostgreSQL persist
GCS clients broadcast
95%
BANDWIDTH SAVED
Structured JSON only — no video streaming over LTE. Cuts uplink requirement to a fraction of comparable telepresence systems.
MESSAGE · TELEMETRY
{
"type": "telemetry" ,
"drone_id": "EQB-01" ,
"ts": 1717938472 ,
"lat": 21.4373 ,
"lon": 40.5127 ,
"alt": 47.2 ,
"battery": 68 ,
"mode": "AUTO" }
MESSAGE · ALERT
{
"type": "alert" ,
"class": "drone" ,
"iff": "UNKNOWN" ,
"lat": 21.4391 ,
"lon": 40.5103 ,
"conf": 0.87 ,
"track_id": 42 }
WSS · TLS 1.3
JSON ONLY
EQAAB · COMMS

## Slide 14
EQAAB · GROUND STATION
SECTION 14 / 24
14
THE OPERATOR'S WINDOW
GCS Dashboard
One pane of glass — map, alerts, telemetry, commands. Built with React + Leaflet.
LATENCY
~1.4S E2E
📷
GCS DASHBOARD SCREENSHOT
Insert real GCS dashboard screenshot — should show the Leaflet map with the active drone marker and flight path, the real-time alert feed, and the telemetry bar with battery / altitude / speed / mode.
REF · EQB-GCS-01
01
Live Leaflet map
Drone position, heading, and flight path rendered in real time over satellite tiles.
02
Alert feed
Streaming list of GPS-tagged detections with class, IFF state, and confidence.
03
Telemetry bar
Battery · altitude · speed · flight mode at a glance.
04
Command panel
RTH · Takeoff · Land · Waypoint upload from the operator's seat.
REACT · LEAFLET · WSS
EQAAB · GCS

## Slide 15
EQAAB · MODEL TRAINING
SECTION 15 / 24
15
FROM DATASET TO DEPLOYED WEIGHTS
Training & Dataset
Reproducible pipeline — open dataset, public framework, single GPU. Result is the best.pt shipped to the drone.
FINAL MAP@50
94.3%
A · DATASET
Composition
Source
Roboflow
Total images
~5,500
Classes
3 (drone · person · car)
Split
80 / 10 / 10
Augmentation
flip · brightness · mosaic · crop
B · TRAINING
Configuration
Platform
Kaggle T4 GPU
Framework
Ultralytics YOLOv8
Base model
yolov8n.pt
Epochs
100
Batch
16
Optimizer
AdamW
📷
TRAINING CURVES
Insert results.png from Ultralytics — loss curves and mAP over 100 epochs.
REF · EQB-TR-01
YOLOV8N · ADAMW
EQAAB · TRAINING

## Slide 16
EQAAB · VERIFICATION
SECTION 16 / 24
16
HOW WE PROVED IT WORKS
Testing Methodology
Four stages — from individual ROS nodes up to live field flights — each with its own tooling and pass criteria.
STAGES
4 LEVELS
STAGE
WHAT WAS TESTED
METHOD
TOOL
UNIT
Individual ROS 2 nodes
Isolated node testing
ros2 launch · pytest
INTEGRATION
Full pipeline data flow
End-to-end message tracing
rqt_graph · terminal logs
SIMULATION
Autonomous mission FSM
Virtual flight
Gazebo · ArduPilot SITL
FIELD
Detection accuracy
Real flights · live targets
Physical drone + GCS
▢
Unit
Each ROS node validated in isolation against mocked inputs.
⇆
Integration
Topic graph traced from camera frame to alert publish.
◉
Simulation
FSM executed virtual missions in Gazebo before real flight.
✈
Field
Eqaab flown against drone, vehicle, and human targets.
V&V · 4 STAGES
EQAAB · TESTING

## Slide 17
EQAAB · METRICS
SECTION 17 / 24
17
WHAT THE PLATFORM ACTUALLY DELIVERS
Results & Performance
Validated across model accuracy, edge inference, and end-to-end alert latency.
STATUS
ALL TARGETS MET
94.3%
MAP @ 0.5
Validation on held-out test split (550 images)
8.3fps
EDGE INFERENCE
On Raspberry Pi 5 · CPU-only · 640px input
91.7%
PRECISION
Averaged across 3 classes, conf ≥ 0.45
~1.4s
ALERT LATENCY
Detection → GCS render, measured end-to-end
PER-CLASS BREAKDOWN
CLASS
PRECISION
RECALL
F1
MAP@50
Drone
0.923
0.901
0.912
0.947
Person
0.914
0.889
0.901
0.938
Car
0.915
0.908
0.911
0.944
Macro avg
0.917
0.899
0.908
0.943
📷
DETECTION SAMPLES
Insert detection example imagery — bounding boxes drawn over real footage of drone, person, and car targets.
REF · EQB-DET-01
KPI · 5/5 PASSED
EQAAB · RESULTS

## Slide 18
EQAAB · LIVE DEMO
SECTION 18 / 24
REC ●
18
THE SYSTEM IN MOTION
Live Demo
Full loop: drone detects target → onboard inference → IFF check → GPS-tagged alert → GCS map updates.
PLAYBACK
~45 SEC
📷
DEMO VIDEO / GIF
Insert the demo recording — should walk through the full chain: drone detecting a target, onboard inference + IFF, GCS receiving the alert, and the map marker updating in real time.
REF · EQB-DEMO-01
A
Detection
YOLOv8 identifies a drone target in the live camera frame; DeepSORT assigns a track ID.
B
IFF + alert
Identifier query fails → target marked UNKNOWN → JSON alert published over WSS.
C
GCS update
Backend relays the alert; React dashboard renders the GPS-tagged marker on the live map.
LIVE RECORDING
EQAAB · DEMO

## Slide 19
EQAAB · ECONOMICS
SECTION 19 / 24
19
PRODUCTION-GRADE FOR 1% OF LEGACY COST
Cost Analysis
A complete intelligent surveillance platform — airframe through cloud — for less than a single high-end CCTV install.
TOTAL BUILD
2,690 SAR
EQAAB · THIS WORK
2,690
SAR · TOTAL
Carbon-fiber frame & motors
820
Pixhawk + PX4 stack
450
Raspberry Pi 5 (8GB)
380
Pi Camera Module
190
GPS · 4G dongle · battery
540
RC receiver · misc.
310
TRADITIONAL SURVEILLANCE
100,000s
SAR
Fixed CCTV + tower install
100k+
Long-range radar
300k+
Piloted UAV system
500k+
Operator staffing (annual)
200k+
Maintenance & comms
recurring
~1%
Production-grade intelligent surveillance at roughly 1% of traditional infrastructure cost — without sacrificing autonomy, identification, or operator control.
BOM · TURN-KEY
EQAAB · COST

## Slide 20
EQAAB · DELIVERY MATRIX
SECTION 20 / 24
20
WHAT WE PROMISED VS WHAT WE DELIVERED
Objectives vs Achieved
Five for five — every committed KPI met or exceeded, each backed by verifiable evidence.
RESULT
5 / 5 ✓
OBJECTIVE
TARGET
ACHIEVED
EVIDENCE
Autonomous flight
Full mission
✓ Verified
Gazebo + field flights
Real-time detection
≥ 5 FPS
✓ 8.3 FPS
RPi5 benchmark · 640px
IFF classification
Friendly / Unknown
✓ Operational
Registry lookup tested
Alert transmission
< 3s latency
✓ ~1.4s
End-to-end measurement
GCS dashboard
Live map + commands
✓ Deployed
React dashboard live
5
OBJECTIVES SET
5
OBJECTIVES MET
2
EXCEEDED TARGET
Detection FPS exceeded target by 66%; alert latency came in at less than half the requirement.
ALL TARGETS · GREEN
EQAAB · DELIVERY

## Slide 21
EQAAB · LESSONS LEARNED
SECTION 21 / 24
21
WHAT BROKE — AND HOW WE FIXED IT
Challenges & Solutions
Three real engineering problems that shaped the final architecture.
PIVOTS
3 MAJOR
01
CHALLENGE
Catastrophic forgetting
Fine-tuning a single YOLOv8 model on the custom drone class measurably degraded its accuracy on the COCO person and car classes — making the model worse at the things it was already good at.
→
SOLUTION
Dual-model parallel architecture
Run the stock yolov8n.pt and the custom best.pt in parallel on every frame, then merge and filter. Each model stays specialised; nothing forgets.
02
CHALLENGE
4G LTE latency for piloting
Manual remote piloting over cellular incurs latency too high for safe low-altitude flight — control-loop lag became unacceptable as soon as we left line of sight.
→
SOLUTION
Fully autonomous FSM
Eliminate the manual control loop entirely. Operator issues high-level commands (RTH, takeoff, waypoints); the FSM executes locally with onboard sensors at deterministic rates.
03
CHALLENGE
CPU-only inference on RPi5
No GPU, no NPU. Larger YOLOv8 variants stalled below 3 FPS — well under our 5 FPS KPI — and risked thermal throttling during long missions.
→
SOLUTION
Nano variant + frame-rate cap
Switched to YOLOv8 nano, capped the inference loop, and kept the input at 640px. Sustained 8.3 FPS with stable thermals and headroom for tracker overhead.
POST-MORTEM · 3 ITEMS
EQAAB · CHALLENGES

## Slide 22
EQAAB · ROADMAP
SECTION 22 / 24
22
WHERE EQAAB GOES NEXT
Future Work
Four directions that build directly on the v1 platform — none require throwing the architecture away.
ROADMAP
V2 · V3
V2 · COORDINATION
Multi-drone Coordination
Multiple Eqaab airframes sharing a single GCS — unified alert feed, deconflicted patrol routes, and cooperative tracking of fast-moving targets.
V2 · SENSOR
Thermal Imaging
Add a thermal payload alongside the RGB camera. Detection at night, through smoke, and against camouflaged targets — same pipeline, fused channels.
V3 · SECURITY
Cryptographic IFF
Replace proximity-based identifier matching with hardware-authenticated transponders. Public-key challenge / response — spoof-resistant by design.
V2 · PERFORMANCE
Edge Optimization
INT8 quantization and structured pruning of the YOLOv8 weights. Target: double the edge FPS without dropping mAP — opens headroom for larger backbones.
ROADMAP · 4 ITEMS
EQAAB · FUTURE

## Slide 23
EQAAB · CLOSING
SECTION 23 / 24
23
WHAT WE BUILT · AND WHO BUILT IT
Conclusion
STATUS
DELIVERED
“ Eqaab demonstrates that a seven-member student engineering team can design, build, and validate a complete production-grade intelligent aerial security platform — integrating autonomous flight, onboard AI, IFF classification, and live operator interfaces into a single cohesive system at a fraction of traditional surveillance cost. ”
7
STUDENTS
24
WEEKS
1
FLYING DRONE
94.3%
mAP @ 50
THE TEAM
Abdulrahman Al-otaibi
Team Lead · Systems Integration
Turki Al-otaibi
Flight Controller · PX4 tuning
Saeed Al-harthi
Perception · YOLOv8 training
Rayan Al-ghamdi
Backend · FastAPI · Postgres
Hossain Al-hubailee
GCS Frontend · React · Leaflet
Mohammed Al-sharif
ROS 2 Mission FSM · IFF
Omar Al-anzi
Hardware Build · Field Testing
MISSION COMPLETE
EQAAB · CONCLUSION

## Slide 24
EQAAB · END OF BRIEFING
SECTION 24 / 24
PROJECT ID 503593
◇ THANK YOU ◇
Q & A
شكراً لكم
We welcome your questions — on architecture, training, comms, IFF, cost, or anything else.
Abdulrahman Al-otaibi
abdulrahman@tu.edu.sa
Turki Al-otaibi
turki@tu.edu.sa
Saeed Al-harthi
saeed@tu.edu.sa
Rayan Al-ghamdi
rayan@tu.edu.sa
Hossain Al-hubailee
hossain@tu.edu.sa
Mohammed Al-sharif
mohammed@tu.edu.sa
Omar Al-anzi
omar@tu.edu.sa
PROJECT ID
503593
TAIF UNIVERSITY
CCIT · CAPSTONE II · 2026
EQAAB · 503593