## Slide 1
HARDWARE
DRONE SOFTWARE — ROS 2
CLOUD BACKEND
GCS DASHBOARD
Pi Camera
12MP · CSI · 30fps
Raspberry Pi 5
8GB · Ubuntu 22.04
Pixhawk
PX4 · IMU · Baro
GPS Module
M8N · ±2m accuracy
4G LTE Dongle
USB · wide-area link
RC Receiver
2.4GHz · HW override
Frame Acquisition
OpenCV · BGR → RGB
YOLOv8n.pt
Person · Car
best.pt
Drone (custom)
Parallel dual-model inference
Merge + Filter
conf ≥ 0.45 · class map
DeepSORT Tracker
Track ID · Kalman · IoU
GPS Fusion
Pixel → lat/lon estimate
IFF Node
Friendly / Unknown?
Discard
Alert Publisher
Mission Manager
FSM · waypoints · failsafe
REST API
GET /alerts · /telemetry
PostgreSQL
JSONB · alerts · telemetry
FastAPI
WebSocket relay
DroneContext
React state hub · WS client
Leaflet.js Map
Live position · path · markers
Alert Feed
Class · confidence · GPS
Telemetry Bar
Battery · Alt · Speed · Mode
Command Panel
RTH · Takeoff · Land · Waypoints
BGR
detections
coords
track ID
target+GPS
Friendly
Unknown
4G LTE
WSS/TLS
persist
WSS
history
cmd
MAVLink
runs
HW override →
→ data flow ⇢ command / control → RC override ◇ IFF decision node
Eqaab — عقاب | System Architecture