## Slide 1
عقاب
EQAAB
Intelligent Autonomous Aerial Surveillance Drone System
GRADUATION CAPSTONE PROJECT · 2026
Presented by the Eqaab Team | Supervised by [Supervisor Name] | [University Name]
CONTENTS
Table of Contents
01
Problem & Solution
Slides 3 – 4
02
System Architecture
Slides 5 – 9
03
Hardware Platform
Slides 10 – 12
04
AI & Detection
Slides 13 – 17
05
Autonomy & Mission
Slides 18 – 20
06
Validation & Results
Slides 21 – 24
07
Conclusions & Future Work
Slides 25 – 27

## Slide 2
01 · PROBLEM DEFINITION
Why Modern Surveillance Falls Short
01
BLIND SPOTS
Fixed cameras and ground patrols leave wide gaps in perimeter coverage — entire approach corridors go unobserved.
02
OPERATOR FATIGUE
Human monitors lose focus after 20 minutes; detection rates drop sharply over multi-hour shifts.
03
SLOW RESPONSE
Manual dispatch chains add 5-15 minutes between sighting and intercept — too slow for fast-moving threats.
04
RADAR LIMITS
Conventional radar struggles to detect small, low-flying UAVs — hostile drones routinely slip through.

## Slide 3
01 · THE EQAAB SOLUTION
From Static Surveillance to Active Defense
THE PROBLEM
THE EQAAB ANSWER
Static cameras with fixed coverage
Mobile aerial platform — flies the perimeter on demand
Human attention degrades over time
AI vision running at 8.3 FPS, no fatigue, 24/7 ready
Manual dispatch chains delay response
Sub-2-second alert latency from detection to GCS
Radar misses small, low UAVs
Custom YOLOv8 model trained specifically for drones
No friend-or-foe discrimination
IFF registry classifies every track, fail-safe to Unknown

## Slide 4
02 · OBJECTIVES & KPIs
Five Measurable Mission Goals
#
OBJECTIVE
SUCCESS CRITERION
ACHIEVED
01
Real-time aerial detection
mAP@50 ≥ 90% on drone class
94.3%
02
On-board edge inference
≥ 8 FPS sustained on RPi 5
8.3 FPS
03
Low-latency alerting
End-to-end alert latency < 2 s
~1.4 s
04
Reliable IFF classification
Fail-safe defaults to Unknown
100% safe
05
Autonomous patrol
Geofenced FSM with failsafes
6 states

## Slide 5
02 · HIGH-LEVEL ARCHITECTURE
Three-Tier System Topology
TIER 1 · EDGE
Drone
· Pixhawk PX4 flight stack
· Raspberry Pi 5 companion
· Pi Camera + GPS module
· ROS 2 (Ubuntu 22.04)
· On-board YOLOv8 inference
TIER 2 · CLOUD
Backend
· FastAPI service
· PostgreSQL database
· WebSocket (WSS / TLS)
· Hosted on Railway
· Alert relay & persistence
TIER 3 · OPERATOR
Ground Control
· React.js dashboard
· Leaflet.js live map
· DroneContext state
· Alert feed + command panel
· Browser-based, any device
4G LTE
JSON
WSS / TLS
WebSocket
Design principle: alerts as structured JSON, not video streams — minimizes bandwidth, maximizes reliability over LTE.

## Slide 6
02 · DRONE-SIDE STACK
ROS 2 Node Topology on the Companion Computer
ROS 2 (Ubuntu 22.04) · Raspberry Pi 5
mission_manager
Owns the FSM. Sets state, issues waypoints to MAVROS, listens for failsafe events.
detection_node
Runs dual YOLOv8 inference + DeepSORT, fuses GPS, publishes track topics.
iff_node
Looks up each track in the IFF JSON registry, tags Friendly or Unknown.
alert_publisher
Serializes alerts to JSON and pushes them over WebSocket via 4G LTE.
INTERFACES
MAVROS
Bridge to PX4 / Pixhawk flight controller
Pi Camera
1080p video frames @ ~10 Hz
GPS Module
NMEA stream → fused into tracks
4G LTE
Outbound WSS connection to backend
RC Receiver
Manual override at any time

## Slide 7
02 · BACKEND & COMMUNICATION
FastAPI · PostgreSQL · WebSocket
CLOUD STACK
FastAPI
Async Python service · REST endpoints + WS handler
PostgreSQL
Persists alerts, registry, mission logs
WebSocket (WSS / TLS)
Bidirectional channel: drone ⇄ backend ⇄ GCS
Railway
Container host with managed TLS + DB
ALERT JSON SCHEMA
alert.json
●●●
{
"drone_id": "eqaab-01",
"timestamp": "2026-04-30T12:34:56Z",
"track_id": 4521,
"class": "drone",
"iff": "unknown",
"confidence":0.87,
"lat": 24.7136, "lon": 46.6753
}

## Slide 8
02 · GCS DASHBOARD
React + Leaflet · Single Source of Truth
DATA FLOW
WebSocket Client
Subscribes to backend WSS
DroneContext
Centralized React state (provider)
UI Components
Map · Alert Feed · Command Panel
Eqaab GCS / Live Operations
LIVE MAP · LEAFLET.JS
ALERT FEED
UNKNOWN
drone · 0.91
12:34:56
FRIENDLY
drone · 0.78
12:31:22
UNKNOWN
person · 0.69
12:28:04

## Slide 9
03 · HARDWARE
Component Inventory
COMPONENT
MODEL / PART
KEY SPEC
ROLE IN SYSTEM
Flight Controller
Pixhawk (PX4)
32-bit · IMU + Baro
Low-level stabilization & motor control
Companion Compute
Raspberry Pi 5
Quad-core ARM · 8 GB RAM
Runs ROS 2 nodes + YOLOv8 inference
Vision Sensor
Pi Camera Module
1080p @ 30 fps
Source frames for detection pipeline
Localization
GPS Module
u-blox · 1 Hz NMEA
Provides position for fused track output
Comms Link
4G LTE Dongle
USB · global coverage
Outbound WSS to backend
Power
LiPo Battery
4S / 5000 mAh
~15 min flight endurance
Manual Override
RC Receiver
2.4 GHz
Pilot can take control at any time

## Slide 10
03 · PHYSICAL BUILD
Assembly & Integration
INSERT BUILD PHOTO
Recommended: 1920×1080 · top-down or 3/4 view of fully-assembled drone
ANNOTATIONS
1
Pixhawk PX4
center plate, vibration-damped
2
Raspberry Pi 5
mounted aft with heatsink + fan
3
Pi Camera
forward-facing on gimbal mount
4
GPS antenna
mast above EMI shielding
5
4G LTE dongle
USB to RPi, external antenna
6
LiPo 4S 5000 mAh
underbelly with strap retention

## Slide 11
03 · DESIGN DECISIONS
Why These Components, Not Others
Why 4G LTE, not Wi-Fi?
CHOSEN
4G LTE Dongle
REJECTED
On-site Wi-Fi mesh
Wi-Fi range collapses past 300 m and depends on infrastructure. LTE gives unrestricted operating radius wherever cellular reaches — the drone can patrol kilometers from base.
Why Raspberry Pi 5, not Jetson?
CHOSEN
Raspberry Pi 5
REJECTED
NVIDIA Jetson Nano / Orin
Pi 5 hits 8.3 FPS on YOLOv8n at a fraction of the cost and weight. Jetson's CUDA acceleration is only worth it above ~20 FPS targets — overkill for our alert-driven design.
Why Pixhawk, not a custom flight stack?
CHOSEN
Pixhawk + PX4
REJECTED
Bespoke flight controller
PX4 has battle-tested stabilization, geofencing, and failsafes built in. Building those from scratch is a graduation project on its own — Pixhawk lets us focus on the AI and ops layer.

## Slide 12
04 · DETECTION PIPELINE
From Pixels to Geo-Tagged Alerts
CAMERA
Pi Cam · 1080p
YOLOv8n
person · vehicle
YOLOv8 best.pt
drone (custom)
MERGE
NMS @ 0.45
DeepSORT
track IDs
GPS FUSION
lat / lon / alt
ALERT
JSON · WSS
DUAL-MODEL YOLOv8 · PARALLEL INFERENCE · CONFIDENCE ≥ 0.45
Why two models?
yolov8n.pt is COCO-pretrained for people/cars. best.pt is custom-trained on drones. Running both in parallel gives full-class coverage without retraining a single combined network.
Why DeepSORT?
Detections alone don't tell you a single drone over time. DeepSORT keeps a stable track ID across frames so we can compute trajectory and emit one alert per object.
Why GPS fusion?
Pixel boxes mean nothing to a ground operator. Fusing the drone's GPS with bounding-box geometry yields a real-world latitude/longitude per track.

## Slide 13
04 · DATASET & TRAINING
Building the Custom Drone Detector
5,500
TOTAL IMAGES
3
OBJECT CLASSES
T4 GPU
KAGGLE COMPUTE
Roboflow
ANNOTATION TOOL
CLASS DISTRIBUTION
drone
2400
person
1700
car
1400
AUGMENTATION & TRAINING
Mosaic
4-image composite per training step
Random scale & flip
horizontal flip + ±50% scale
HSV jitter
robustness to lighting / weather
100 epochs
AdamW · batch 16 · img 640

## Slide 14
04 · MODEL PERFORMANCE
Validation Metrics on Held-Out Set
94.3%
mAP@50
91.7%
PRECISION
89.2%
RECALL
8.3
FPS @ RPi 5
TRAINING CURVES (PLACEHOLDER)
epochs →
mAP@50
recall
PER-CLASS mAP@50
drone
94.8%
person
95.1%
car
92.9%

## Slide 15
04 · IFF SYSTEM
Identify Friend or Foe — Fail-Safe by Design
New Track Detected
In IFF Registry?
YES
FRIENDLY
tag · log · suppress
NO
UNKNOWN
alert · operator review
FAIL-SAFE
Lookup error → defaults to UNKNOWN
IFF JSON REGISTRY (SAMPLE)
iff_registry.json
{ "friendlies": [
{ "id": "EQAAB-01", "type": "drone" },
{ "id": "ALPHA-7", "type": "drone" },
{ "id": "PATROL-3", "type": "vehicle" }
] }
DESIGN RULES
Registry hot-reloads — no drone restart needed
Unknown is the default — no entry, no friendly status
Operator may promote / revoke at runtime via GCS
All classifications are logged for forensic review

## Slide 16
04 · OBJECT TRACKING & GEO-FUSION
DeepSORT + GPS = Real-World Coordinates
DEEPSORT
Multi-object tracking with appearance features
Kalman filter
predicts each track's next bbox from velocity
Hungarian matching
associates new detections with existing tracks
Appearance embedding
ReID features prevent ID swaps when objects cross
Track lifecycle
tentative → confirmed → lost — IDs persist across occlusions
GPS COORDINATE CALCULATION
From bounding box to latitude/longitude
Drone GPS
(lat, lon, alt)
Target on ground
projected lat / lon
Camera FOV
PROJECTION (simplified)
offset = altitude · tan(angle from nadir)
(target_lat, target_lon) = (drone_lat, drone_lon) + offset_vec

## Slide 17
05 · AUTONOMOUS FLIGHT
Mission Finite-State Machine
01
IDLE
start
02
TAKEOFF
alt OK
03
PATROL
threat
04
TRACK
clear / RTL
05
RETURN
reached home
06
LAND
mission complete / reset to IDLE
IDLE
Disarmed, waiting for GCS command
TAKEOFF
Climb to mission altitude (typ. 30 m)
PATROL
Follow waypoints, run detection loop
TRACK
Lock onto Unknown target, hold position
RETURN
RTL to home GPS coordinate
LAND
Controlled descent + disarm

## Slide 18
05 · MISSION MANAGEMENT
Geofencing · Waypoints · Failsafes
GEOFENCE PERIMETER
WP1
WP2
WP3
WP4
HOME
FAILSAFE CONDITIONS
Geofence breach
Auto RTL to home immediately
RC link loss > 5 s
Pilot loop hold, then RTL
Backend WSS loss
Continue mission, queue alerts
GPS quality poor
Abort patrol, hover and alert
Battery < 25%
Force RETURN state
Manual override
RC takes priority over autonomy

## Slide 19
06 · SIMULATION VALIDATION
Gazebo + ArduPilot SITL
GAZEBO WORLD
3D environment + sensor simulation
[ INSERT SCREENSHOT ]
ARDUPILOT SITL
Software-in-the-loop flight stack
[ INSERT SCREENSHOT ]
6/6
FSM transitions verified
100%
Geofence breach → RTL
~50
Simulated mission runs

## Slide 20
06 · TESTING METHODOLOGY
Three-Tier Verification Strategy
01
UNIT
Component-level
ROS 2 node pytest suite
IFF lookup edge cases
JSON schema validation
FSM transition tests
Mock GPS / mock camera
70+ test cases
02
INTEGRATION
Subsystem chains
Detection → IFF → Alert path
Drone ⇄ backend WSS handshake
Backend ⇄ GCS event delivery
FSM under simulated failures
Loopback latency measurement
12 scenarios
03
FIELD
Real-world flights
Outdoor patrol over open area
Drone-vs-drone detection
LTE handoff between cells
Geofence breach trial
Multi-target scenarios
Live flights

## Slide 21
06 · DETECTION RESULTS
Sample Detections from Field Trials
drone 0.91
[ INSERT DETECTION FRAME ]
Drone @ 80 m
class: drone · conf: 0.91
IFF: UNKNOWN
person 0.87
[ INSERT DETECTION FRAME ]
Person on perimeter
class: person · conf: 0.87
IFF: —
car 0.79
[ INSERT DETECTION FRAME ]
Vehicle approach
class: car · conf: 0.79
IFF: —

## Slide 22
06 · END-TO-END PERFORMANCE
System Latency · Reliability · Throughput
~1.4 s
ALERT LATENCY
detection → GCS
8.3
FPS @ EDGE
RPi 5 sustained
94.3%
DETECTION mAP
on validation set
98.7%
WSS UPTIME
during field trials
LATENCY BUDGET
Inference
480 ms
Track + IFF
220 ms
LTE + WSS
600 ms
End-to-end ≈ 1400 ms · well under the 2-second target
WebSocket auto-reconnect kept alert delivery at 98.7% during cell-tower handoffs in field tests.

## Slide 23
07 · KNOWN LIMITATIONS & MITIGATIONS
What Didn't Fully Work — and How We Handled It
LIMITATION
MITIGATION
Night & low-light detection
Pi Camera struggles below ~5 lux — drone class accuracy drops materially after dusk.
Documented as daytime-only system. Thermal imaging upgrade scoped for future work.
FPS ceiling at 8.3
On-board RPi 5 cannot match desktop GPU throughput; smaller fast targets may slip between frames.
Confidence threshold tuned (0.45) and DeepSORT re-association recovers most missed frames.
LTE coverage gaps
Some patrol corridors hit dead zones; alerts back up briefly while the WSS reconnects.
Alert queue persists locally on the Pi; replays automatically when WSS reconnects (98.7% delivery).
IFF spoofing risk
JSON registry has no cryptographic signing — a hostile actor could in principle inject a fake friendly ID.
Treated as out-of-scope for v1; signed/cryptographic IFF is the first item on the future-work list.

## Slide 24
07 · OBJECTIVES vs ACHIEVED
Scoreboard
OBJECTIVE
STATUS
EVIDENCE
Real-time aerial detection
MET
mAP@50 = 94.3% on validation set
On-board edge inference
MET
8.3 FPS sustained on Raspberry Pi 5
Low-latency alerting
MET
End-to-end ≈ 1.4 s, target was < 2 s
Reliable IFF classification
MET
Fail-safe path verified in unit + field tests
Autonomous patrol FSM
MET
6-state FSM with 6 failsafe triggers
Night-time detection
PARTIAL
Daytime only — thermal in future work
Multi-drone coordination
DEFERRED
Out of v1 scope; flagged for future work
5 of 5 in-scope objectives MET. 2 stretch goals deferred to future work — clearly scoped for v2.

## Slide 25
07 · FUTURE WORK
The Roadmap to v2
01
MULTI-DRONE SWARM
Mesh communication between drones, distributed patrol assignment, and automatic hand-off when one returns to base for battery.
02
THERMAL IMAGING
Add a FLIR Lepton sensor for night and low-light detection; train a thermal-domain branch alongside the RGB models.
03
CRYPTOGRAPHIC IFF
Replace plain JSON registry with signed challenge/response IFF. Eliminates the spoofing attack surface called out in our limitations.
04
EDGE OPTIMIZATION
TensorRT/ONNX export, INT8 quantization, and a Coral USB accelerator path to push sustained FPS toward 15+ on the same airframe.

## Slide 26
THANK YOU
شكراً لكم
QUESTIONS & DISCUSSION
THE EQAAB TEAM
[Member 1] · Hardware & Flight Stack [Member 2] · AI / Detection [Member 3] · Backend & GCS
Supervised by [Supervisor Name] · [University Name] · contact@eqaab.example